## Slide 1
Interdisciplinary Centre for Security, Reliability and Trust
Signal Processing Applications in Radar and Communications
SPARC Research Group
Waveform Design in Modern Radar Systems
Bhavani Shankar M. R
16 April 2026
Hosted by:
Centre for Networked Intelligence, IISc

## Slide 2: Acknowledgements
Colleagues at SPARC
Collaborators at IEE

## Slide 3: Outline
Modern Radar Systems
  Applications, Requirements and Degrees of Freedom
SISO Radar Waveform Design
  Waveform Properties, Ambiguity functions, Design Objectives
  Waveform Optimization Methodologies
Examples
  PMCW
  Quadratic Phase waveforms for interference mitigation
  Principle of Stationary Phase
MIMO Waveforms
  Orthogonality
  Extension of SISO design
ISBN: 9781630818920
Artech House, 2022

## Slide 4
Modern Radar Systems
SISO Radar Waveform Design
Examples
MIMO Radar Waveforms
Outline

## Slide 5
Heinrich Hertz : Experimental proof of existence of Electromagnetic waves
Fundamental contribution, series of developments
  mmWave generation, influencing radio as communication medium – J. C. Bose
  Radio transmissions – Marconi
  Telemobiloscope – Radio waves for detection/ ranging – Hulsmayer
The Radar Origins
Notes: NEED TO MAKE IT MORE COLORFUL

## Slide 6
The Radar Evolution
Size
Cost
Metric waves to mmWave and THz
Capabilities

## Slide 7
Modern Radar Systems

## Slide 8
Distributed Radar System
Reference sensor and camera
Sensor 2
Sensor 1
Point cloud display
Connection

## Slide 9
Data Collection
Department of General Pediatrics and Neonatology, Saarland University Medical School,
Homburg, Germany.
Vital Sign Monitoring
Breathing, Heartbeat estimation
  Heartrate variability
Applications
  Neonatal care monitoring
  In-cabin monitoring
  Assisted living technologies
  Security
  “Search-and-Rescue”
Heart Rate: 80 b.p.m

## Slide 10
Multi-modal Fusion
Radar
Can measure range/speed
Can see through medium
Not affected by weather
Lidar
Can generate high resolution 3D points
Sensitive to weather
Cannot see through medium
Limited range
Why not combine both for a system that is bigger than the sum of their parts?

## Slide 11
A brief digression with multiple sensors
Oncoming Traffic
Cruise Control
Un co-ordinated transmissions: Interference in Roadside scenarios

## Slide 12
Short(er) Range
High Resolution
Many non-stationary Targets
Multiple and potentially un co-ordinated
© Ant PC Systems
New Scenarios, Challenges and DoF
Available Degrees of Freedom
    Multiple antennas and Waveform Diversity
    Multiple sensors and Spatial Diversity
    Receiver Processing Algorithms

## Slide 13
Modern Radar Systems
SISO Radar Waveform Design
Examples
MIMO Radar Waveforms
Outline

## Slide 14: Classical Pulse Doppler Radar Processing
Electromagnetic wave is characterized by amplitude, frequency, and polarization
When an incident wave interacts with the object of interest, all these properties change
Single antenna transmit pulse train:
Reflections from L targets, each defined by
Received signal:
Design Trade-Offs
High range resolution requires short time transmissions/ large signal bandwidths
High Doppler resolution requires long dwell times
High angular resolution is achieved with more antenna element
Delay-Doppler map
Reflectivity
Range-time
Doppler

## Slide 15
Short pulses
  have good range resolution
  Decreased average power  Limited receive SNR  Decreased detection
Dilemma
  Average power pulse width
  Resolution 1/ pulse width
Requirement
  Energy of a long pulse + resolution of a short pulse
  Use of a waveform
Waveform: structured modulation of the pulse, typically in frequency/phase and sometimes also in amplitude (AM).
Waveforms
Pulse Width,
Square Pulse
Bandwidth =
Time × Bandwidth =
Pulse Width,
Linear Frequency Modulated Waveform
Bandwidth =
Time × Bandwidth =
Frequency
Frequency
Pulse Width,
Bandwidth =
Time × Bandwidth =
Phase Coded Waveform

## Slide 16
Ambiguity Functions
Ambiguity function contains information on:
  range resolution
  range sidelobe level
  range ambiguity spacing
  Doppler resolution
  Doppler sidelobe level
  Doppler ambiguity spacing
Ideal ambiguity function : thumbtack –
  i.e. an infinitely-narrow spike at the origin
  infinitely-high resolution in range and Doppler
  no sidelobes, and no ambiguities
Transmitted Waveform
Received Waveform
Receiver filter :
Output of the receiver filter at time
Ambiguity Function

## Slide 17
Ambiguity Functions
Square pulse
FMCW
© Radartutorial, Pics from internet

## Slide 18
Ambiguity Functions of FMCW
© Radartutorial, Pics from internet

## Slide 19
Ambiguity Functions
  Smaller main lobe
  High sidelobes in range, 13 dB peak side lobe
    Reminiscent of rectangular pulse
  Classical method to reduce side lobes
    Windowing at receive side
      Mismatched Filter – SNR loss
    Amplitude Modulation at the transmit
      Widowing at transmit
      Amplifier inefficiency

## Slide 20
Ambiguity Functions
Phase Code
© A generalized multivariate Student-t mixture model for Bayesian classification and clustering of radar waveforms (researchgate.net)
M- length Barker Code:
Max Peak Side Lobe Main lobe/ M
© Radartutorial, Pics from internet

## Slide 21
FMCW or PMCW?
FMCW
PMCW
FMCW radars sample @ few MHz
e.g : 16.7 Msps
Highly popular
PMCW radars sample @ BW
e.g : 275 Msps
Performance of both are largely similar
PMCW offers additional degrees of freedom

## Slide 22
Waveform Design Problems
Quantity | Mathematical Expression
Phase Code | 
Aperiodic Autocorrelation | 
PSL | 
ISL | 
Constraints
  Energy
  Peak-to-Average Power Ratio (PAPR, PAR)
  Unimodularity (being Constant-Modulus)
  Finite or Discrete-Alphabet (integer, binary, m-ary constellation)
  …

## Slide 23
Waveform Design Objectives
  Integrated Sidelobe Level (ISL)
Small
PSL
ISL
avoid masking of weak targets in range sidelobes of a strong return
mitigate the deleterious effects of distributed clutter echoes which are close to the target of interest
  Peak Sidelobe Level (PSL)

## Slide 24
Waveform Design Problems
ISL Minimization
PSL Minimization
Many of these problems are shown to be NP-hard, others are deemed to be difficult
How to handle these problems in good time?

## Slide 25
Waveform Optimization techniques
Gradient-Descent Based Methods (GD)
Majorization-Minimization (MM)
Coordinate Descent (CD)
Alternating Direction Method of Multipliers (ADMM)
Block Successive Upper-bound Minimization (BSUM)
Several others ...
Notes: Time-Staggered FMCW Waveform: More efficient than alternative transmitting

## Slide 26
Modern Radar Systems
SISO Radar Waveform Design
Examples
MIMO Radar Waveforms
Outline

## Slide 27
Waveform Design in an automotive setting
Oncoming Traffic
Cruise Control
Un co-ordinated transmissions: Interference in Roadside scenarios

## Slide 28
FMCW and interference
Notes: Which Scenario

## Slide 29
Example 1 : Waveform Design Based Approach
Key Idea
Divide a PMCW sequence into subsequences
  Each radar could use its own subsequence lengths
Devise polynomial phase in each subsequence
Different radars can use different phases
Notes: Which Scenario

## Slide 30
*Integrated/Peak Sidelobe Level (ISL/PSL)
Let the sequence X be partitioned into L sub-sequences
Every sub-sequence has a length Ml where l = 1,..,L
Every sub-sequence is expressed as
Polynomial phase behavior in every sub-sequence:
is the Qth degree polynomial phase coefficients of the lth sub-sequence
Solved using Majorization-minimization (MM) framework
Problem Statement

## Slide 31
Interference Robustness
Statistical Interference Analysis
Notes: Statistical Inteference Analysis

## Slide 32
USRP Setup

## Slide 33
Parameter Settings and setup
Table: Radar sensor parameters for victim and interferer sensor
Calculate SINR of the known target
Victim radar operates with an interferer in FoV
Proposed waveform compared with LFM in every transmit pulse
Receive signal from the target and the interferer was independently digitally delayed in software
Experiment was conducted in a controlled environment in an anechoic chamber

## Slide 34
Results – Category 1: LFM (victim) <-> LFM (Interferer)
Victim waveform†
Interferer waveform
Received signal
Dechirp signal
Range profile

## Slide 35
Results – Category 2: PECS (victim) <-> LFM (Interferer)
Received signal
Dechirp signal
Range profile
Victim waveform
Interferer waveform†

## Slide 36
Results – Category 3: Optimized (victim) <-> Optimized (Interferer)
Received signal
Dechirp signal
Range profile
Victim waveform†
Interferer waveform†

## Slide 37
Spectrum
Time-Domain via inverse Fourier
Can we design with constraints on and
Example 2 : Parametric NLFM
Key Idea
    Want to have a certain shape in time domain
    Want to have certain shape in the spectrum
    Can both be possible?
Spectrum
Time-Domain via inverse Fourier

## Slide 38
Example 2 : Parametric NLFM
Key Idea
    Want to have a certain shape in time domain
    Want to have certain shape in the spectrum
    Can both be possible?
Spectrum
Time-Domain via inverse Fourier
M. Follmann, M. Alaee-Kerahroodi, B. S. M. R, V. Lücken and A. R. Diewald, "Accuracy Estimation of Window-Based Nonlinear Frequency-Modulated Waveforms," in IEEE Transactions on Radar Systems, vol. 3, pp. 1287-1297, 2025, doi: 10.1109/TRS.2025.3606111

## Slide 39
Important Regions of Integration of Oscillating Function
Approximate around this point

## Slide 40
The Principle
Stationary Phase
is some solution
Taylor Expansion
After manipulations
Integrations
Frequency domain phase
Time-domain phase
E. Fowle, “The design of FM pulse compression signals,” IEEE Trans.
Inf. Theory, vol. IT-10, no. 1, pp. 61–67, Jan. 1964.

## Slide 41
Instantaneous Frequency of Different Window Function Waveforms
Endpoints

## Slide 42
Designed Waveform
Final Time-Domain Formulation
Waveform Parameters:
: Time-Domain Waveform
: Pulse Duration
: Bandwidth
: Fourier Parameters
: Window Parameters

## Slide 43
K=2 parameters
Spectral Domain
Waveform Parameters
: Window Function
: Bandwidth
: Window Parameters
: Waveform Parameters
: First order Bessel Funciton

## Slide 44
Results
LFM: g = [1],
Hann: g = [(1/2); (1/2)],
Hamming: g = [(25/46); (21/46)].
The custom window uses g = [(9/14); (5/14)].

## Slide 45
Validity
ESD of the generated waveform for g = [(25/46); (21/46)].

## Slide 46
Design Flexibility
PSLR, ISLR, and scaled MLW for a one parameter window with g1 = 1- g0.

## Slide 47
Modern Radar Systems
SISO Radar Waveform Design
Examples
MIMO Radar Waveforms
Outline

## Slide 48
Resolution
Image resolution
© https://hullabaloo.co.uk/blog/high-res-low-res-make-sure-digital-images-suitable-print/
"Higher resolution" means more image details
Range Resolution =
Spatial Resolution =
Bandwidth
Aperture size
(azimuth/elevation Resolution)
The minimum separation between two targets that permits them to be distinguished by a radar
Radar resolution
Resolution is defined in each of the dimensions of measurement
Typically range, azimuth, elevation
High resolution required in Range, Speed (?), Azimuth, and Elevation
mmWave radar is used for the accurate sensing of location, velocity, and angle
Increase signal Bandwidth!
Increase Aperture size!
General rule to improve radar resolution

## Slide 49
Increasing Aperture Size
7 X 5 Real Array
16 Tx, 16 Rx leading to 16 x 16 Virtual array

## Slide 50
MIMO Radar
Virtual Array
Tx Array
Rx Array
To be separated in the receive side and form a virtual array without a grating lobe, the transmit waveforms must be orthogonal to each other(waveform diversity) – MIMO radars
MIMO Radars : New problems
  How to design waveforms?
  How to set-up the arrays?

## Slide 51
MIMO Orthogonal Waveforms
Time Division Multiplexing (TDM)
  Alternative Transmitting: transmission capabilities of all transmit antennas are not fully utilized
  Doppler Angle coupling; multiplexing can be optimized to increase unambiguous Doppler
  Possibility to be implemented with dechirping technique and consequently low sampling rate ADCs
Frequency Division Multiplexing (FDM)
  Fast-time: range-angle coupling will occur after MIMO beamforming
  Slow-time: causes that the unambiguous PRF reduced by number of antennas
  Possibility to be implemented with dechirping technique and consequently low sampling rate ADCs
Doppler Division Multiplexing (DDM)
  Causes that the unambiguous PRF reduced by number of antennas
  Possibility to be implemented with dechirping technique and consequently low sampling rate ADCs
Code Division Multiplexing (CDM)
  Intra-pulse coding: high range sidelobes depending on the cross-correlation property of the code sequence. High ADC sampling rate is required – possibility to synthesize the equivalent FMCW and implemented by dechirp.
  Inter-pulse coding: causes that the unambiguous PRF reduced by number of antennas- possibility to be implemented with dechirping technique and consequently low sampling rate ADCs
Notes: Time-Staggered FMCW Waveform: More efficient than alternative transmitting

## Slide 52
Waveform Design Problems
Quantity | Mathematical Expression
Phase Code from antenna | 
Set of MIMO waveforms as a matrix | 
Autocorrelation between waveforms of antenna and antenna | 
ISL | 
PSL | 
Quantity | Mathematical Expression
Set of MIMO waveforms as a matrix | 
ISL | 
PSL | 
Constraints
  Similar to SISO

## Slide 53
Summary
Waveform design enables enhanced performance in multiple use cases
Difficult optimization problems  motivates use of novel iterative techniques
  Data driven?
Have not looked in detail at MIMO/ ISAC/ RIS.
Notes: Time-Staggered FMCW Waveform: More efficient than alternative transmitting

## Slide 54
SPARC Track record
Projects
  2 EC (ERC Advanced & ERC Proof-of-Concept)
  6 National projects – Fundamental Research (1 bilateral with Germany), 2 National projects – Collaboration with Industry
  1 US Airforce Overseas Research Lab Grant
Personnel
  19 @ End of current hiring: 10 PhD, 4 Post Docs, 2 Research Scientists, 1 Developers, 1 Research Fellow, 1 Assistant Prof
  Alumni : Academia (Prof UIC USA, Research Fellow NTU-Singapore), Industry (Valeo, Barkhausen, Amphinicy, IEE)
  Members from academia, industry (Embraer, Continental, ..)
Dissemination
  3 Edited Books / > 30 Journals / 5 Book Chapters / >50 Conferences, 6 patents
  Tutorials: 15
  Prototype Demonstrations: 5
Interaction with industry
  Actively leading the strategic partnership with IEE (www.iee.lu ) since 2015
  8 industry PhD students
  2 National Projects
Distinctions
  Special mention : Barry Carlton Award from IEEE TAES
  Student paper finalists IEEE Radar Conference 2019, 2025
  Best Thesis Award for Vital Sign Monitoring, University of Luxembourg, 2023

## Slide 55
Expertise in radar signal processing, electromagnetics, systems modelling, wireless communications and hardware.
https://www.uni.lu/snt-en/research-groups/sparc/
Signal Processing Applications in Radar and Communications (SPARC)

## Slide 56
Research @ SPARC
Radar
Multiple antenna Radar
Distributed Radar
Sensing and Communications
Sensor Fusion
Simulators & Prototypes
Interior & Exterior

## Slide 57
End to End approach
Basic Research
Industrial Research
Simulators
Theory
Prototype

## Slide 58
Interdisciplinary Centre for Security, Reliability and Trust
@SnT_uni_lu
SnT, Interdisciplinary Centre for
Security, Reliability and Trust
Connect with us
Bhavani Shankar
Assistant Professor & Team Lead
Bhavani.Shankar@uni.lu
SPARC: https://www.uni.lu/snt-en/research-groups/sparc/
http://radarmimo.com