## Slide 1
Human Automation Teams for Decision Making: Impact of Task load on Team Performance
Kesav Ram Kaza
(Research fellow)
University of Ottawa
April 8, 2025
CNI, IISc Bengaluru.
by

## Slide 2
Agenda
  Human Automation Teams
    Human Factors?
    Decision Referrals in Teams - Problem Formulation
    Optimal Referral Strategy - Analysis and Simulation
    Experimental Study
  Application in Counter Drone Surveillance [briefly]
    Framework
    Experimental Study

## Slide 3
Agenda
  Human Automation Teams
    Human Factors
    Decision Referrals in Teams
    Impact of Task load on Team Performance
    Experimental Study
  Applications in Counter Drone Surveillance
    Framework
    Experimental Study

## Slide 4
Human Automation Teams
Automation has come into the domains of both physical (manufacturing, assembly, etc) and mental tasks (data analysis and decision making)
Automation and humans have different models of decision making
  Automation is good at number crunching
  Humans are good at reasoning with quick mental models (??)
  Humans are good at generalization (??)
  In collaborative decision making both these strengths can be utilized.
Background

## Slide 5
Human Automation Teams
Search and Rescue Missions
Skimming through large amounts of data such as video footage, heat signatures, etc
Reconnaissance and intelligence for defence purposes
  Identification of hostile targets
  Automated mine detection
(Semi)-Autonomous navigation systems
Motivating Applications for Human-AI teaming

## Slide 6
Human Automation Teams
Setup
In Human-Automation Teams for decision making,
  most task processing done by AI.
AI supervisor refers some to human for fresh analysis and final decision.
In a given set of tasks first processed by AI, how many and which tasks must be referred to the human?
Decision Referrals in Human-Automation Teams
Automation
Human Reviewer
Supervising
System

## Slide 7
Human Factors
Physical and mental consequences for actions
Mental Workload
Fatigue
Belief, Trust in Automation
Self-Confidence
Human Factors affecting Performance

## Slide 8
Human Factors
All these factors are complex cognitive constructs.
Hidden variables with multiple state definitions.
Lot of debate in psychology and human-factors literature.
Human Factors affecting Performance

## Slide 9
Human Factors
The notion of mental workload is needed to answer questions of practical importance such as the following.
  How busy is an operator?
  How complex are the tasks that an operator needs to perform?
  Can any additional tasks be handled by the operator?
  Will the operator be able to respond to unexpected events?
Cognitive or Mental Workload in the Literature
C. D. Wickens, J. G. Hollands, S. Banbury, and R. Parasuraman,
Engineering psychology and human performance. Psychology Press,
2015.

## Slide 10
Human Factors
Varied notions across literature
Definitions are based on models involving mental resources such as memory and attention.
  “Low workload levels have been associated with boredom and decreased attention to task, whereas high workload levels have been associated with increased error rates and the narrowing of attention to the possible detriment of other information or tasks" [NASA-STD-3001 Technical Brief]
Measurement models
  Self report measures
  Physiological (or neurophysiological) measures
  Primary task performance measures
Cognitive or Mental Workload in the Literature
Longo, Luca, et al. "Human mental workload: A survey and a novel inclusive definition."
Frontiers in psychology 13 (2022).

## Slide 11
Human Factors
Varied notions across literature
Definitions are based on models involving mental resources such as memory and attention.
  “Low workload levels have been associated with boredom and decreased attention to task, whereas high workload levels have been associated with increased error rates and the narrowing of attention to the possible detriment of other information or tasks" [NASA-STD-3001 Technical Brief]
Measurement models
  Self report measures
  Physiological (or neurophysiological) measures
  Primary task performance measures
Cognitive or Mental Workload in the Literature
Longo, Luca, et al. "Human mental workload: A survey and a novel inclusive definition."
Frontiers in psychology 13 (2022).

## Slide 12
Human Factors
Mental workload (MW) is a complex cognitive construct.
Task load - Defined as the number of tasks per session or fraction of tasks from a batch in a fixed period of time.
MW might be a non-linear function of task load along with other variables
MW is a system state that is not directly observable.
Can task load can be used as a handle on MW?
Mental workload vs task load

## Slide 13
Human Factors
Under some conditions (?): can use task load as a descriptor of the mental workload.
This simplifies the model and avoids measurement problems.
Model the human as task load dependent performer.
Mental Workload vs Task load

## Slide 14
Human Automation Teams
Human Side
Human as interventionist
  may redo some tasks completed by automation.
  may interrupt tasks of robot.
Human as non-interventionist
  may or may not adhere to assigned task load.
Task allocation planning problem classes
Automation Side
Blind task allocation
  focussed on optimal workload distribution, does not look at the tasks before allocation.
  assigned based on estimated “mean” cognitive state or expected performance of the human.
Informed task allocation
  looks at each and every task to decide.

## Slide 15
Human Automation Teams
Human Side
Human as interventionist
  may redo some tasks completed by automation.
  may interrupt tasks of robot.
Human as non-interventionist
  may or may not adhere to assigned task load.
Task allocation planning problem classes
Automation Side
Blind task allocation
  does not look at the tasks before allocation.
  assigned based on estimated “mean” cognitive state or expected performance of the human.
Informed task allocation
  looks at each and every task to decide.

## Slide 16
Agenda
  Human Automation Teams
    Introduction to Human Factors
    Decision Referrals in Teams - Problem Formulation
    Optimal Referral Strategy - Analysis and Simulation
    Experimental Study
  Applications in Counter Drone Surveillance
    Framework
    Experimental Study

## Slide 17
Human Automation Teams
Binary classification tasks
The automation takes a first look at the batch of tasks
It decides which subset of tasks need to be referred to human for review and final decision
For all the other tasks (), the automation makes the final classification decision
Problem statement : Given a batch (set) of binary classification tasks find the
  “optimal” subset of tasks to be referred to the human.
Decision Referrals in Teams for Classification Tasks
Automated Classifier
Human Reviewer
Supervisor
Batch
Decide
Classification Decisions

## Slide 18
Human Automation Teams
Problem statement : Given a batch (set) of binary classification tasks find the
  “optimal” subset of tasks to be referred to the human.
Device an indexing scheme to rank the tasks.
Then, show that the indexing scheme is optimal.
First, we pose the problem as an optimization problem.
Objective of total cost minimization .
  Total cost = Cost of automation classification decisions + penalty for referrals + Cost of human classification decisions.
What is the plan?
Automated Classifier
Human Reviewer
Supervisor
Batch
Decide
Classification Decisions

## Slide 19
Human Automation Teams
For each task , the human decides between and based only on the observation
Human does not have access to the automation’s observation
The human also does not account that the automation referred the task after looking at the entire batch
At the minimum task load the human is better than the automation.
At the highest task load the human is worse.
Human Decision Models - Assumptions

## Slide 20
Human Automation Teams
System Model
Supervisor
Batch of Tasks
Referral Strategy
Classification Decisions
Observation model
Observation model
Decision model
Decision model
Automation
Human
Task load
Dependence

## Slide 21
Human Automation Teams
System Model
Supervisor
Batch of Tasks
Referral Strategy
Classification Decisions
Observation model
Decision model
Automation
Difficult or
Unavailable
Observation model
Decision model
Human
Task load
Dependence

## Slide 22
Human Automation Teams
System Model
Supervisor
Referral Strategy
Classification Decisions
Observation model
Task load dependent classifier performance model
Decision model
Automation
Human
Just use what can be
measured
Batch of Tasks

## Slide 23
Human Automation Teams
System Model
Supervisor
Referral Strategy
Classification Decisions
Observation model
Task load dependent classifier performance model
Decision model
Automation
Human
Batch of Tasks
{TPRs, FPRs}
task load set

## Slide 24
Human Automation Teams
System Model and Notation
Supervisor
Task batch
State of task is
Referral Strategy
Classification Decisions
Observations
Decisions
Based on
Automation
Human
Observations
Decision set
satisfying
the Perf. Model
Perf. Model
Automation’s expected classification decision cost
Human’s total expected classification decision cost

## Slide 25
Human Automation Teams
System Model and Notation
Supervisor
Task batch
State of task is
Referral Strategy
Classification Decisions
Observations
Decisions
Based on
Automation
Human
Observations
Decision set
satisfying
the Perf. Model
Perf. Model
Automation’s expected classification decision cost
Human’s total expected classification decision cost

## Slide 26
Human Automation Teams
Observation and Performance Models : Example
Automation Observation Model - Static
Human Observation Model - Task load dependent
are AWGN.

## Slide 27
Human Automation Teams
Observation and Performance Models : Example

## Slide 28
Human Automation Teams
Gaussian models are used in the literature to represent decision making under uncertainty.
Also relevant in applications involving high dimensional inputs (such as images) classified using neural networks.
  The weights and input to the output layer may be assumed to be Gaussian by applying a mean field approximation [Schoenholz 2022].
Gaussian Observation Models
S. S. Schoenholz, J. Gilmer, S. Ganguli, and S.-J. Dickstein, “Deep
information propagation,” in International Conference on Learning
Representations, 2022.

## Slide 29
Human Automation Teams
We consider only costs of the final decisions on tasks.
Classification decision costs:
  Depend on the (mis)match between the decision makers choice and the actual hypothesis of a task
The cost of classification decision for task is
Values of etc, depend on the application.
For example in defence scenarios, and in medical applications in scenarios where mistreatment is dangerous.
Problem Formulation - Decision Costs

## Slide 30
Human Automation Teams
The automation makes classification decisions ,
The expected cost of automation's decision for task is
Automation’s Decision Costs

## Slide 31
Human Automation Teams
The automation makes classification decisions ,
The expected cost of automation's decision for task is
Automation’s Decision Costs

## Slide 32
Human Automation Teams
The automation makes classification decisions ,
The expected cost of automation's decision for task is
Automation’s Decision Costs

## Slide 33
Human Automation Teams
Cost of human classification decisions depends on
  the automation’s posterior beliefs of tasks
  the performance model of the human.
Expected human classification cost is linear in posterior belief.
Total expected human classification cost for the referred subset is
Human Decision Cost

## Slide 34
Human Automation Teams
Given the posterior beliefs of the automation, and the decision distributions of the human , determine and so as to minimize the total cost .
Total cost = Cost of automation classification decisions + penalty for referrals + Expected Cost of human classification decisions.
Optimization Problem

## Slide 35
Human Automation Teams
Numerical Example
Numerical illustration of the decision costs for
The black lines represent the cost of the automation, as a function of the posterior probability of hypothesis .
The other lines show the expected cost for the human, , for , with .
The cost reduction for referring task to the human is , which is the difference between the black lines and the others.

## Slide 36
Agenda
  Human Automation Teams
    Introduction to Human Factors
    Decision Referrals in Teams - Problem Formulation
    Optimal Referral Strategy - Analysis and Simulation
    Experimental Study
  Applications in Counter Drone Surveillance [briefly]
    Framework
    Experimental Study

## Slide 37
Human Automation Teams
Define G-index:
R-index of a task is the expected cost reduced by referring it to the human under task load w.
Theorem: For tasks represented by and a given task load to minimize , it is optimal to allocate the tasks with the highest R-indices to the human.
  The total expected cost is equivalent to minimizing
Optimal Decision Referral Strategy under fixed task load

## Slide 39
Human Automation Teams
The optimal task load can be identified by evaluating the optimal for all choices of
There are only possible values of task load .
We can do an exhaustive search to find
If there are additional assumptions such as decreasing TPR and FPR with w, more efficient algorithms can be devised.
Optimal Decision Referral Strategy

## Slide 40
Human Automation Teams
Blind Allocation (BA) : BA uses a fixed task load optimized using a priori performance models for the automation and the human, and refers tasks arbitrarily to the human.
  is based on cost per classification task by each agent
Optimal Allocation (OA) or the Optimal Referral Strategy:
  Based on relative cost of uncertainty/risk (rep. by ) of all tasks in the batch.
Static Allocation: A fixed task load variant of the optimal allocation.
Proposed Referral Strategies

## Slide 41
Human Automation Teams
Blind Allocation (BA) : BA uses a fixed task load optimized using a priori performance models for the automation and the human, and refers tasks arbitrarily to the human.
We have
and are the a priori expected classification decision cost per task for the automation and for the human operator under task load w respectively.
Can be computed offline by the automation.
Blind Allocation

## Slide 42
Human Automation Teams
SA finds and optimal constant task load value as follows:
    Here is the minimum of for fixed task load .
the expectation in can be computed by Monte-Carlo simulations over a large number of batches.
Further, upon seeing a batch of tasks, SA refers the tasks with the highest R-indices to the human.
Static Allocation

## Slide 43
Human Automation Teams
Summary of Proposed Strategies
 | Blind Allocation | Optimal Allocation | Static Allocation
Allocation dependent on human capability? | Yes, for the task loads. No, for individual tasks. | Yes | Yes
Task load | Constant across batches | Varies with batches | Constant across batches
Computation | Offline | Online | Task load computed offline. Optimal task subsets computed online.

## Slide 44
Human Automation Teams
Assume Gaussian Observation Models
Human observation model has task load dependent noise variance
Assume that human is an threshold classifier with decision rule
Numerical Simulations
is the threshold in the observation space.

## Slide 45
Human Automation Teams
Numerical Examples
Comparison of referral policies for 25 distinct problem instances, assuming the human has a Gaussian observation model. The batch size is K = 20. [left] Both OA and SA have similar performance and better
average decision cost than BA. [right] The task load under BA shows large variations across instances.

## Slide 46
Human Automation Teams
Numerical Examples
[left] Simulated average (TPR, FPR) points for each task load and their inter-quartile ranges obtained from several randomly generated sets of 5 sample batches for each task load. [right] Distribution of expected optimal task load allotted by OA strategy to the human operator across all the sets.

## Slide 47
Human Automation Teams
Insights from Simulation Study
SA and OA have similar performance.
We need to compare OA and BA in a more realistic setting.
The simulations suggest that consecutive task load levels must be chosen such that mutual conflation is avoided while accommodating an estimation error tolerance ϵmax < 0.1 on both sides.
This might be achieved at least 5 measurements for each task load.
The number of human participants for TPR, FPR estimation can be decided based on this information.

## Slide 48
Agenda
  Human Automation Teams
    Introduction to Human Factors
    Decision Referrals in Teams - Problem Formulation
    Optimal Referral Strategy - Analysis and Simulation
    Experimental Study
  Applications in Counter Drone Surveillance [briefly]
    Framework
    Experimental Study

## Slide 49
Human Automation Teams
Experimental Study with Human Subjects
Experimental setup: A simulation of a radar screen showing multiple mobile targets.
Clicking a target displays information such as speed, altitude, etc, on the central pane.
The operator has to decide the correct label (Hostile or Non-hostile)
and presses one of the two classification buttons.

## Slide 50
Human Automation Teams
Experimental Setup
Our study uses a simulation environment for threat evaluation closely imitating the S-CCS microworld (Simulated Combat Control System) described in Lafond 2009.
Participants monitor a simulated radar display with a set of mobile targets represented as dots on the screen,
Each of which is either Hostile or non-hostile .
If the operators always follow the decision tree correctly, an average accuracy of approximately 90 % is achieved.
At higher task loads the operators might make mistakes when following the tree or be unable to complete all the tasks, reducing the accuracy.
The participants are asked to try and label all the targets in the allotted time .
D. Lafond, J. Champagne, G. Hervet, J.-F. Gagnon, S. Tremblay, and R. Rousseau, “Decision analysis using policy capturing and process tracing techniques in a simulated naval air-defense task,” Human Factors
and Ergonomics Society Annual Meeting, vol. 53, no. 18, pp. 1220–1224, 2009.

## Slide 51
Human Automation Teams
Experimental Study with Human Subjects
To evaluate the practical effectiveness of the proposed referral policy.
Experiment 1 - Parameter Estimation
  Participant group size - 28 = 19 males + 9 females
  Valid samples - 18
  Valid sample threshold - Completion of 55 % of the provided tasks
Experiment 2 - Comparison of Optimal Allocation vs Blind Allocation
  Participant group size - 15 = 7 males + 8 females
  Valid samples - 15
$ 25 compensation for one hour experiment session

## Slide 52
Human Automation Teams
Experimental Study with Human Subjects
Experimental setup: A simulation of a radar screen showing multiple mobile targets.
Clicking a target displays information such as speed, altitude, etc, on the central pane.
The operator follows the decision tree to decide the correct label (Hostile or Non-hostile)
and presses one of the two classification buttons.

## Slide 53
Human Automation Teams
Experiment 1 - Parameter Estimation
Need to estimate TPR and FPR for different task loads.
27 two minute rounds with batch sizes 6, 9, 12, or 15 tasks in each round.
Rest after each round as needed by the operator and click ‘Next’.
First three rounds are for training and are not used for the estimation.

## Slide 54
Human Automation Teams
Experiment 1: Estimation of Human TPR and FPR
Experiment 1: [left] TPR and FPR measurements from all 28 participants for four task loads 6,9,12,15, with inter-quartile (IQR) ranges along with the outliers. [right] Comparison of empirical estimates from 18 valid samples (who completed at least 55% of all allocated tasks) to simulation based estimates made prior to the experiment.

## Slide 55
Human Automation Teams
Experiment 2 - OA vs. BA
To compare OA and BA we used an independent participant group.
A ``within-subject'' experiment design was used.
That means, each operator is presented multiple rounds with tasks referred by BA policy, as well as rounds with tasks referred by OA policy.
Overall, each operator goes through a sequence of 24 two-minute rounds, 12 each for BA and OA in random order.
Batch size K=30 is was used in all rounds.
BA policy maintains a fixed task load across all batches.

## Slide 56
Human Automation Teams
Experiment 2: Statistical Analysis
Experiment 2 - Performance measurements (inter-quartile ranges)
of blind allocation and optimal allocation policies for all participants.
Null Hypothesis: ,
Alternate Hypothesis: .
Paired t-test conducted to compare performances.
Worst case analysis: t-statistic of 4.99 and p-value of 0.0002

## Slide 57
Human Automation Teams
Conclusion
Three referral strategies were proposed.
The proposed methods only requires the true and false positive rates of the ``human classifier'' as a function of task load.
  rather than a model of human decision making.
Results show that OA performs significantly better than BA.
SA may provide similar performance in applications where frequent changes in human task load are undesirable.

## Slide 58
Human Automation Teams
Conclusion
In practice, the automation classifier is trained on a large amount of labelled data, but its performance may degrade when there is a domain or distribution shift during the deployment.
Human performance may remain almost the same as they are naturally capable of “generalization to out-of-distribution”.
Hence, the choice must be made based on the application scenario.

## Slide 59
Agenda
  Human Automation Teams
    Introduction to Human Factors
    Decision Referrals in Teams - Problem Formulation
    Optimal Referral Strategy - Analysis and Simulation
    Experimental Study
  Applications in Counter Drone Surveillance [briefly]
    Framework
    Experimental Study

## Slide 60
Application
Application to Counter Drone Networks
Enhancing Counter Drone Operations Through Human-AI Collaboration: A Hierarchical Decision-Making Framework
Problem Space
Data Acquisition and Test Setup
Radar and Optical Data
System Architecture
Results
Pub.: 42nd DASC, 2023.

## Slide 61: Problem Space
Application
Application to Counter Drone Networks
Enhancing Counter Drone Operations Through Human-AI Collaboration: A Hierarchical Decision-Making Framework
Radar
PTZ
AI Engine
GCS
Ground detection-classification
Human Operator

## Slide 62
Application
Application to Counter Drone Networks
Experiment Setup
Pan Tilt Zoom (PTZ) camera
Resolution-1920X1080
Pan- 360°
Tilt- -90° to 45°
Zoom- 32x optical zoom, 12x digital
FMCW Radar
Range resolution- 3.25m
Velocity resolution- 0.91m/s
Azimuth resolution- ±1°
Elevation resolution- ±3°
Update rate 10 Hz

## Slide 63: Radar and Optical Data
Total Radar data:
12 hours of UAV Tracks 2 hours of Birds Tracks
1 hour of other ground targets (car, human) tracks.
Total optical data:
85 videos with 207,663 UAV frames.
Sample trajectory of (a) bird and (b) UAV captured by the ground radar system. The (c) and (d) depict samples of a bird and a UAV, respectively, extracted from the PTZ video data.
The range of operation: 50m to 1.2 km
DASC, 2023.
Application

## Slide 64
Application
Application to Counter Drone Networks
System Model
Overall system architecture for the proposed drone detection and classification framework. The system integrates multiple sensors, including ground radar and a PTZ camera, and employs a human-AI collaboration framework for efficient and accurate surveillance.

## Slide 65
Application
 | Predicted Drone | Predicted OFO
True Drone | 94% | 6%
True OFO | 58% | 42%
Examples of true positive and false positive results obtained from the optical classifier. The top row shows instances where the classifier accurately detects and classifies UAVs, while the bottom row depicts cases where the classifier incorrectly identifies non-UAV objects as UAVs.
Precision |  | 
0,49 | 0,36 | 0,25
Radar classifier
The classifier model integrates classical Interactive Multiple Model tracking (IMM) filter features and trajectory based features.
Radar classifier confusion matrix
Optical detector and classifier performance

## Slide 66: Referrals to Human using OA
Application
Sample tasks referred to the human under the constraint that 5 tasks must be allocated to the human. All tasks referred to the human reviewer contained false positives of the AI detector. In the last one (bottom right), the UAV was missed by the detector, but a bounding box was drawn elsewhere in the frame. In the other cases, bounding boxes were falsely drawn by the detector with no flying objects in the frame.
TPR | FPR
88% | 22%

## Slide 67
POTENTIAL FUTURE WORK
Real time decision support systems.
Complex tasks that require memory, attention and executive function.
Compound tasks involving heterogenous subtasks.
Modelling fatigue along with mental workload.

## Slide 68
POTENTIAL FUTURE WORK
How can such a real time DSS be verified (model, simulation based and statistical verification)?
  How can we say that a DSS reduces risk and not increase it?
  And with how much confidence?

## Slide 69
Related Articles
K. Kaza, J. Le Ny, A. Mahajan, “Decision Referrals in Human Automation Teams: Impact of Taskload on Team Performance,” under review, IEEE Trans. on Human Machine Systems.
V. Mehta, K. Kaza, F. Dadboud, M. Bolic, I. Mantegh, “Enhancing Counter Drone Operations Through Human-AI Collaboration: A Hierarchical Decision-Making Framework,” 42nd DASC 2023 .
K. Kaza, J. Le Ny, A. Mahajan, “Decision Referrals in Human Automation Teams,” 60th IEEE CDC 2021.

## Slide 70: Thank You!

## Slide 71
Human Factors
How are they assessed?
Usually measured though feed back from human operators.
Different scales based on different sets of questions asked.
Examples are Bedford scale and NASA TLX
Bedford scale - uni dimensional 10−point scale to measure operator’s spare mental capacity while completing a task.
NASA TLX - A multi-dimensional scale based on feedback regarding mental demand, physical demand, temporal demand, effort, performance, frustration level.
Cognitive or Mental Workload

## Slide 72
Human Factors
Schematic: Relationship among primary-task resource demand, resources supplied, and performance, indicating the “red line” of workload overload
[source: Wickens et al 2015].
Cognitive Workload

## Slide 73
Human Factors
Schematic: Over-load and under-load can be detrimental to task performance. Operators may become less likely to attend to potentially important sources of information and fail at the task.[source: NASA-STD-3001 Tech. Brief]
Cognitive Workload

## Slide 74
Research Work (Post-Doctoral Fellowship)
How mentally demanding was the task?
How physically demanding was the task?
How hurried or rushed was the pace of the task?
How successful were you in accomplishing what you were asked to do?
How hard did you have to work to accomplish your level of performance?
How insecure, discouraged, irritated, stressed, and annoyed were you?
NASA-TLX Questions

## Slide 75
Research Work (Post-Doctoral Fellowship)
Brief discussion of Dubois and Le Ny 2020.
• Human-automation team presented with batches of classification tasks sequentially.
• Automation suggests a fraction of tasks to be carried out by the human.
• Human’s classification performance is a function of workload (taskload).
• The human completes these tasks and may take up more depending on his/her
cognitive state (trust).
• Markovian evolution model for cognitive states.
• MDP/POMDP based approach to maximize long term performance.
Task allocation with human intervention

## Slide 76
Research Work (Post-Doctoral Fellowship)
A possible family of ROC curves for a human classifier, based on the equal variance Gaussian model [Dubois and Le Ny 2020].
Task allocation with human intervention

## Slide 77
Human Factors
Decision Referrals in Human-Automation Teams

## Slide 78
Human Automation Teams
Static Allocation (SA) - fixed task load variant of optimal policy: Assuming that all the referred tasks must be completed by the human in a fixed amount of time, variations in task load across different batches can induce stress and fatigue, degrading human performance.
Since this aspect was not taken into account when deriving OA for a single batch, a policy like SA with constant task load might have an advantage in practice.
Static Allocation (SA)